# Text boxes

MAR-2000

# AFTER LANDING CHECK

APU	ON	CPLT

TRANSPONDER & RADAR	STBY & OFF	CPLT

FLAPS	UP	CPLT

LIGHTS AND STROBES	AS REQUIRED	CPLT

PROBES	OFF	CPLT

BLEEDS	SET	CPLT

### IN RANGE CHECK

## PRESSURIZATION 	SET	PF

FUEL	CHECKED	PF

ALTIMETERS	SET	BTH

CAS	CHECKED / CLEAR	BTH

#### LANDING DATA	SET	BTH

###### APPROACH BRIEFING	COMPLETE	PF

# APPROACH BRIEFING

“This will be an ____ approach, on runway ___ at ___ ,

ILS/VOR selected  freq. ____ , ident ____ ,

Course selector set to ____,

ADF1 selected to ____ , freq. ___ , ident ____ ,

ADF2 selected to ____ , freq. ___ , ident ____ ,

(if applicable)Check no flags

Bearing Pointer 1 selected to ____ ,

Bearing Pointer 2 selected to ____ ,

Procedure turn altitude is ____ ,

Final Approach Fix altitude is ____ ,”

LEGEND

PILOT		PLT

COPILOT		CPLT

PILOT FLYING		PF

PILOT NON FLYING		PNF

BOTH CREW MEMBERS		BTH

FIRST FLIGHT OF THE DAY		*

### SHUT DOWN CHECK

## CHOCKS & BRAKES	(AS REQUIRED)	PLT

ELECTRICS / GENERATORS	SET	PLT

*FUEL CHECK VALVE	CHECKED	PLT

THRUST LEVERS	SHUT OFF	PLT

#### PAX SIGNS	SEAT BELTS OFF	PLT

###### ANTI ICE	WING & COWLS OFF	PLT

###### FUEL PUMPS	OFF	PLT

HYD. PUMP 3A	(AS REQUIRED)	PLT

BEACON	OFF	PLT

###### NW STEERING	OFF	PLT

# FLIGHT COMPARTMENT SAFETY INSPECTION

CIRCUIT BRAKERS	CLOSED	PLT

NW STEERING	OFF	PLT

HYDRAULIC PUMPS	OFF	PLT

LANDING GEAR LEVER	DOWN	PLT

SPOILER LEVER	RETRACTED	PLT

THRUST LEVER	SHUT OFF	PLT

FLAP LEVER	SET TO FLAP POS.	PLT

RADAR	OFF	PLT

ADG MANUAL RELEASE	STOWED	PLT

BATTERY MASTER	ON	PLT

BATT. VOLTAGE / FIRE FAIL	CHECKED	PLT

APU FIRE TEST	(AS REQUIRED)	PLT

APU	(AS REQUIRED)	PLT

AC ELECTRICS	ESTABLISH	PLT

AIR CONDITIONING	(AS REQUIRED)	PLT

IRS / AHARS BOTH	NAV/MAG	PLT

EMERGENCY EQUIPMENT	CHECKED	PLT

GEAR & SAFETY PINS	ON BOARD	PLT

AIRCRAFT DOCUMENTS	CHECKED	PLT

WHEN NOSE AREA IS CONFIRMED CLEAR

HYDRAULIC PUMP 3A	ON	PLT

NOSE WHEEL DOOR	CLOSED	PLT

FMS INITIALIZATION	COMPLETE	PLT

CHIEF PILOT

SIGNATURE

FOR TRAINING PURPOSES ONLY

### TERMINATING CHECK

## CHOCKS & BRAKES	IN & OFF	PLT

IRS	OFF	PLT

THRUST REVERSERS	OFF	PLT

NW STEERING	OFF	PLT

EMERGENCY LIGHTS	OFF	PLT

#### WINDSHIELD HEAT	OFF	PLT

###### CARGO FAN	OFF	PLT

###### PACKS	OFF	PLT

BLEEDS	ALL OFF	PLT

HYDRAULIC PUMPS	ALL OFF	PLT

EXTERNAL LIGHTS	ALL OFF	PLT

APU GENERATOR	OFF	PLT

APU START / STOP	OFF	PLT

APU POWER / FUEL	OFF	PLT

BATTERY MASTER	OFF	PLT

DC SERVICE	OFF	PLT

DOME LIGHT	OFF	PLT

###### BOARDING LIGHTS	OFF	PLT

### 10.000 FOOT CHECK (DESCENT)

## APU & BLEEDS 	SET	PNF

LIGHTS & PAX SIGNS	(AS REQUIRED)	PNF

LANDING DATA

WX-WGHT / V-SPEEDS/ N1-REF / FMS/ 3 RADIOS/QNH /LNG-ELV

### BEFORE LANDING CHECK

## FLIGHT ATTENDANT 	ADVISED	PF

PAX SIGNS	BOTH ON	PF

THRUST REVERSERS	ARMED	PF

LANDING GEAR	DOWN	PF

FLAPS	(DEGREES) AND INDICATING	PF

NON PRECISION

VOR-NDB-LOC-BC-GPS

“Minimum is ____ , MDA set on  PFD MAP is ____ ,

Call me 100’ above and minimums

At minimums, I will call Landing OR Go Around at the MAP

In the event of a Go around, I will... (the published missed approach procedure, or as otherwise “cleared”, is stated)”

PRECISION

ILS

“Decision height is ____ , MDA set on  PFD,

Call me 500’ above Aerodrome 100’ above  minimums and minimums

At minimums, I will call Landing OR Go Around

In the event of a Go around, I will... (the published missed approach procedure, or as otherwise “cleared”, is stated)”

REQUIREMENTS: APU, ANTI-ICE, IGNITION, RADAR

REV  - 1

F-CR

F-CR

RD

RD

F-CR

RD

RD

PILOT CHECKLIST

NORTH AMERICAN

CL- 65

100 / 200

REV  - 1 MAR-2000